## Slide 1
Production management system specifications
Documentation EN Blueprint for YAMATO
Blueprint
R9
Made for: Yamato Electric (Thailand) Co., Ltd.
By: TOMAS TECH CO.,LTD.
Version 23/May/2025
Confidential

## Slide 2
Revision History
Date | Version | File name | Details
15/Jun/2024 | R1 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | First edition
15/Jul/2024 | R2 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Second edition
4/Aug/2024 | R3 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Third edition
14/Aug/2024 | R4 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Fourth edition
21/Aug/2024 | R5 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Fifth edition
7/Sep/2024 | R6 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Sixth edition
12/Dec/2024 | R7 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Seven edition
12/May/2025 | R8 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Eighth edition
23/May/2025 | R9 | Production management system specifications Documentation EN Blueprint for YAMATO Blueprint | Ninth edition
2
3
4
5
6
7
8
9

## Slide 3
■Contents
1. Overview
2. Overall configuration diagram
3. Document image
3-1. Importing Files
3-1-1. BOM (Sample)
3-1-2. Delivery Schedule (Shipment plan)
3-1-3. Forecast Monthly
3-1-4. Remain PO
3-1-5. Master plan (Production plan)
3-2. Print label information
3-3. Location Tag
3-4. Labeling
4. Schedule
4-1. Work Flow Chart
4-1-1. CSV file import process
4-1-2. Warehouse Inbound/Incoming process
4-1-3. Goods Receive Process
4-1-4 QC Process
4-1-5. Picking Process (Part Store)
4-2. Stock management
4-3. Outbound
4-4. Master management
5. System functional specifications
5-1. Handy terminal function
5-2. Handy terminal function Inbound
5-3. Handy terminal function Outbound
5-4. Handy terminal function Stock Management
5-5. PC operation flow Basic
5-6. PC operation flow Schedule
5-7. PC operation flow Inbound
5-8. PC operation flow Outbound
5-9. PC operation flow Stock management
5-10. PC operation flow Master management
6. Q&A
7. Sign off

## Slide 4
1. Overview
Introduced Production management system to YAMATO.
The system specifications for introduction are described in this document.

## Slide 5
Inbound label
Input Data
2. Overall configuration diagram
Represents a configuration diagram of the stock management system. It is a configuration image of hardware and documents.
Overall configuration diagram image
Inbound
Stock management
Outbound
Able to import the materials data in format of CSV file.
Purchase order (30 days advanced)
Forecast
Production plan
Pegasus Server
Handy terminal× 10
Label printer × 1
WS412 (WH)
Plan data (IN/OUT)
LAN cable
WIFI
PO
Forecast
Label printer × 1
WS412 (Injection&Press& Molding&Remain)
Label printer × 1
WS412 (ASSY)
Mobile printer × 1
PW2NX (WH)
WIFI
4
5

## Slide 6
2. Overall configuration diagram
Pegasus
server
Handy terminal#1
Lan cable
Wi-Fi
Network diagram
YAMATO office
YAMATO Warehouse
Label printer #1
Switching hub
Client pc
Access Point
Handy terminal#10
Label printer #2
Label printer #3
Mobile printer #1
Bluetooth
4

## Slide 7
2. Overall configuration diagram
Hardware diagram
Pegasus
server
Handy terminal#1
YAMATO office
YAMATO Warehouse
Switching hub
Client pc
Access Point
Handy terminal#10
AC220V*1
AC220V*1
Charger #1
Charger #10
AC220V*10
Label printer #1
Label printer #2
Label printer #3
Lan cable
Wi-Fi
Bluetooth
AC220V*1
AC220V*1
AC220V*1
Mobile printer#1
Charger #1
AC220V*1
4

## Slide 8
3. Document image
3-1. Importing Files
Item | File name | Type | Remarks
Inbound / Material Receive | Remain PO.xls | Purchase Order | Import to Pegasus (p.12)
Outbound / Delivery / Production plan | HOSODA & LOCAL DELIVERY SCHEDULE OF JUNE'2024.xls | Delivery Plan | Shipment Plan Import to Pegasus (p.10)
 | Plan_Assy_Inj_Press.xlsx | Production Plan | Production plan Import to Pegasus (p.13)
Master / Report / Other | BOM Sample.xlsx | BOM | * Must be change format (p.9)
 | Japan shipment Request.xlsx | Forecast Monthly | Use this format for Forecast Monthly (p.11)
4

## Slide 9
3. Document image
3-1-1. BOM (Sample)
YAMATO ⇒Pegasus
No | Product | FG Code | Part code | Part name | Material code | Material grade/size | Usage | BOM | Com | Unit price | Supplier
1 | KYUHAI | FG7173 | FP190910090001 | PL COVER | M12220137S | FP994 | 0.00366 | 1 | 3 |  | 
2 | KYUHAI | FG7173 | FP190965040000 | CASE | M720965010001 | UREA CU6600Y70LT (GREEN) | 0.02850 | 1 | 3 |  | 
3 | KYUHAI | FG7173 | FP190965050000 | CAM | M720965010001 | UREA CU6600Y70LT (GREEN) | 0.00350 | 1 | 3 |  | 
4 | KYUHAI | FG7173 | FP190965070000 | HIKIDAMA | M12220136S | PP COMPOUND E701G | 0.00101 | 1 | 3 |  | 
5 | KYUHAI | FG7173 | FP190965080000 | NAME RING | M12210563S | ABS COMPOUND QF-N | 0.00471 | 1 | 3 |  | 
6 | KYUHAI | FG7173 | P190910050000 | LEVER |  |  |  | 1 | 3 |  | 
7 | KYUHAI | FG7173 | P190910060000 | CAME PLATE |  |  |  | 1 | 3 |  | 
8 | KYUHAI | FG7173 | P190910070000 | HIKITE |  |  |  | 1 | 3 |  | 
9 | KYUHAI | FG7173 | P190910120000 | KOTEIHEN A |  |  |  | 1 | 3 |  | 
10 | KYUHAI | FG7173 | P190910130000 | KOTEIHEN B |  |  |  | 2 | 3 |  | 
11 | KYUHAI | FG7173 | P190910160000 | FLAT SPRING |  |  |  | 1 | 3 |  | 
12 | KYUHAI | FG7173 | P190910170000 | SPRING A S91017 |  |  |  | 1 | 3 |  | 
13 | KYUHAI | FG7173 | P190910180000 | SPRING B S91018 |  |  |  | 1 | 3 |  | 
14 | KYUHAI | FG7173 | P190911020000 | C RING |  |  |  | 1 | 3 |  | 
15 | KYUHAI | FG7173 | P190965020000 | SPL REVET |  |  |  | 1 | 3 |  | 
16 | KYUHAI | FG7173 | P190965060000T | (KYUHAI SW KADOHEN) | MP11526004S | C5210R-EH 0.4 X 28 | 0.00248 | 1 | 2 |  | 
17 | KYUHAI | FG7173 | P190965070000 | SHAFT |  |  |  | 1 | 3 |  | 
18 | KYUHAI | FG7173 | P190965100000 | STEEL COVER |  |  |  | 1 | 3 |  | 
19 | KYUHAI | FG7173 | P190965120000 | STRING A 1.6*910 |  |  |  | 1 | 3 |  | 
20 | KYUHAI | FG7173 | P190965140000 | NAME PLATE |  |  |  | 1 | 1 |  | 
21 | KYUHAI | FG7173 | P300015010000 | HATOME 1.8*4 |  |  |  | 4 | 1 |  | 
22 | KYUHAI | FG7173 | P300015540000 | SCREW TP 3*8(THAI) |  |  |  | 2 | 3 |  | 
23 | KYUHAI | FG7173 | PK081000000000 | BOX KYUHAI SWITCH ( SET ) |  |  |  | 0.005 | 3 |  | 
24 | KYUHAI | FG7173 | W190910230000 | LEAD WIRE A |  |  |  | 1 | 3 |  | 
25 | KYUHAI | FG7173 | W190910240000 | LEAD WIRE B |  |  |  | 1 | 3 |  | 
*Must be change format below table
No | FG Code | Ref part | Part no | Part name | Usage | Unit | Level | Supplier Code | Supplier Name
1 | FG7173 | FG7173 | FP190910090001 | PL COVER | 1 | Pcs | 1 |  | 
2 | FG7173 | FP190910090001 | M12220137S | FP994 | 0.00366 | Kgs | 2 |  | 
3 | FG7173 | FG7173 | FP190965040000 | CASE | 1 | Pcs | 1 |  | 
4 | FG7173 | FG7173 | M720965010001 | UREA CU6600Y70LT (GREEN) | 0.02850 | Kgs | 2 |  | 
2
2
Example of BOM file
L0/L1
L2
L3
6

## Slide 10
3. Document image
3-1-2. Delivery Schedule (Shipment plan)
YAMATO ⇒Pegasus
YAMATO ELECTRIC (THAILAND) CO., LTD. |  |  |  |  |  |  |  |  |  | 
HOSODA & LOCAL DELIVERY SCHEDULE OF JUNE'2024 |  |  |  |  |  |  |  |  |  | 
RV_00 |  |  |  |  |  |  |  |  | UPDATE: | 13-May-24
Sum of PO Q'TY |  |  |  |  |  | YDT REPLY |  |  |  | 
CUS'T | Material No. | FG Code | Product Name | Inv. No. | PO. NO. # | 5-Jun-24 | 6-Jun-24 | 7-Jun-24 | 17-Jun-24 | TTL
TPT | 6233002003 | FG-8275 | MS-27ET | 2400067 | 10000583658 |  |  | 12000 |  | 20000
 | 17438000014366@MD |  |  | 2400067 | 10000586969 |  |  | 8000 |  | 
TTEI | NEBI10830000000 | FG-2932 | POWER PUMP PLK-BA,10V | 2400065 | 2202402174 |  | 2000 |  |  | 3000
 | NEMI10000000001 | FG-2932 | POWER PUMP PLK-BA,10V | 2400066 | 2202402174 |  | 1000 |  |  | 
 | PCBI6236019401T | FG-8172 | SDD | 2400063 | 2202406926 | 1500 |  |  |  | 1500
 | PCBI6236033501T | FG-8102 | GDD | 2400063 | 2202403916 | 3900 |  |  |  | 21000
 |  |  |  | 2400063 | 2202405785 | 6600 |  |  |  | 
 |  |  |  |  | 2202405785 |  |  |  | 8400 | 
 |  |  |  |  | 2202407555 |  |  |  | 2100 | 
 | PCBI6343177901T | FG-8103 | SENSOR CASE GDD | 2400064 | 2202403916 | 2000 |  |  |  | 14000
 |  |  |  | 2400064 | 2202405785 | 4000 |  |  |  | 
 |  |  |  | 2400064 | 2202407555 | 2000 |  |  |  | 
 |  |  |  |  | 2202407555 |  |  |  | 6000 | 
 | PCBI6343198201T | FG-8104 | 3 SENSOR CASE GDD | 2400064 | 2202405785 | 8000 |  |  |  | 14000
 |  |  |  |  | 2202405785 |  |  |  | 4000 | 
 |  |  |  |  | 2202407555 |  |  |  | 2000 | 
*Create the delivery outbound schedule only. It can be outbound the items from any store location.
2
*User will add the Japanese customer to this file.
Noted on 23May2024
1. User can search the items by Inv no/Po no.
2. Update invoice no instructions (might not included when import)
2.1 Manual edit or enter the invoice no on Pegasus
2.2 Import the invoice no map with po no and material
3. It can’t be delivery outbound if there has no invoice number.
4. There are multiple invoice numbers with the same PO no.
2
Customer
TPT
TTEI
HOSODA
Customer | Forecast | PO
Japan | 4 months | 3 months
Thai | 2 weeks – 1 month | 2 weeks – 1 month
Forecast / PO plan
8

## Slide 11
3. Document image
3-1-3. Forecast Monthly
YAMATO ⇒Pegasus
*May including all shipment requests with this format
4

## Slide 12
3. Document image
3-1-4. Remain PO
YAMATO ⇒Pegasus
*Used to create Material Inbound
2
*An item can be received from vary suppliers.
2

## Slide 13
3. Document image
3-1-5. Master plan (Production plan)
YAMATO ⇒Pegasus
*Import this file to generate the material outbound and inbound work job for production.
** The jobs will be created before one shift time or one day earlier than the actual production time.
2
Process time generate
- Day shift (-1 day)
- Night shift (same day)
Assy plan should be separate the Qty column to DAY and NIGHT shift.
8

## Slide 14
3. Document image
3-2. Print label information (Warehouse)
55mm
85mm
DATE : 6-Jun-23
TIME: 08:30 SEC: PC
SUPPLIER : AMP USER ID : EX1234
PART CODE : FPT20530101
PART NAME : BODY 3P (WH) Injection
QUANTITY : 1,500 PCS. LOT: 20231231
123456789001
QC/QA : CHECK
INSPEC ID: QC0001 PASS
REMARK : REJECT
SPECIAL USE
Font : Consolas
Item definition
DATE : Date of print label
TIME : Time of print label
USER ID : Printing user
SEC : Department user
SUPPLIER : Supplier No
PART CODE : Part No
PART NAME : Part Name
QUANTITY : Current part stock number
Unit : Unit of label quantity e.g. PCS
LOT : Lot number
LABEL ID : Label ID number
QR information
[PART CODE] │[LOT] | [SERIAL NO] | [LABEL ID]
PART CODE : Part No
LOT : Lot number
SERIAL NO : Serial no (box no)
LABEL ID : Label ID number
YDT
2
2
* There are 2 types background color Black/White. For solving the swap problem while repack the package
5
6
8
**QC inspection results PASS : When all quantities have passed
REJECT : When the quantity is NG SPECIAL USE : When some quantity passes

## Slide 15
3. Document image
3-3. Location Tag
Font : Consolas
Item definition
LOCATION CODE : Location ID
QR information
[LOCATION CODE] │[ITEM CODE1],[ITEM CODE2],…
LOCATION CODE : Location ID
ITEM CODE 1…n : Item code that allows placement of items (leave blank
for a free location).
6
60mm
55mm

## Slide 16
3. Document image
3-4. Labeling
2
Process | Area | Remaining Label | New Label
Repack | - | M | M
Sale | - | M | -
Inbound Material * | WH | - | A/M
Inbound FG/NG ** | Production | - | M
Schedule Picking Warehouse | WH | A | A
Schedule Picking Production | Production | A | -
Crusher *** | Injection | - | M
* Use the receive item qty from plan and should be adjustable
** Manual print and enter the qty by lot size(produce QTY plan) and should be adjustable
*** Create crusher label regarding the user can control the crusher stock
A : Automatic print / M : Manual print

## Slide 17
4. Operation flow
YAMATO
Production Management System Pegasus
Purchasing Instruction (P.24)
FG production plan
Material/WIP qty check
Notification if not enough
Check in process PO
NG Report
Handy function
Pegasus report
Stock check
4-1. Schedule
HT : Stock Check
HT : NG Report

## Slide 18
4. Operation flow
4-1. Inbound
Manage inbound status using the following 3 steps or 4 steps.
Inbound Completed
Schedule registered
Inbound working
Cancel
Inbound Completed
Schedule registered
8
QC process
Inbound working
Inbound QC
Inbound material
Inbound production

## Slide 19
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-1. CSV file import process
Production Management System Pegasus
Planning the production
Schedule from Purchase Order
Import the planning on Pegasus
CSV
Verify and Confirm
Finish

## Slide 20
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-2. Warehouse Inbound/Incoming process
Production Management System Pegasus
Return to supplier
Start
Yes
QC Check?
No
4-1-3.Material receive
process
Return?
Yes / No
Finish
No
Yes
8

## Slide 21
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-3. Material Receive Process (process by WH)
Production Management System Pegasus
Put label to items.
Finish
Start
Yes
Check daily job?
Check Qty & Prepare part label
Inbound process scan label by handy
No
Place the items to WH Location
7
QC Check?
Return to supplier
Yes
Return?
Yes / No
Finish
No
Yes
8
1
8
3
500
KGS
Qty
100
KGS
NG
2
9
9
600

## Slide 22
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-4. Production issue FG to WH (Process by Assy)
Production Management System Pegasus
Put label to items.
Finish
Start
Yes
Check daily job?
Inbound process scan by handy
No
Store in the area of ​​ASSY
Inbound Item
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
1
Date
From
Supplier
code
Input the quantity of items produced.
3
Print labels based on QC results via Handy
Quality inspection by QC.
600
KGS
Qty
8
0
KGS
NG
2
9
600
4
600
KGS
Qty
0
KGS
NG

## Slide 23
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-5. Production issue WIP to WH (Process by Injection & Press)
Production Management System Pegasus
Put label to items.
Finish
Start
Yes
Check daily job?
Inbound process scan by handy
All done?
No
Yes
Store in the area of ​​Injection / Press
No
Inbound Item
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
1
Date
From
Supplier
code
Input the quantity of items produced.
Print labels according to QC results
Quality inspection by QC.
8
Input the quantity of items after Finishing or Tapping.
8
2
580
KGS
Qty
20
KGS
NG
Select the next process
QC
Finishing or Tapping
3
9
4
500
KGS
Qty
60
KGS
NG
4
500
KGS
Qty
60
KGS
NG

## Slide 24
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-6. Confirm schedule (Confirm FG/WIP Receive by WH & Confirm Material Receive by PD)
Production Management System Pegasus
Finish
Start
Yes
Production issue FG to WH?
Confirm inbound by handy
All done?
No
Yes
Move to location fix ID that displays on HT
No
Confirm Inbound
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
1
Date
From
Supplier
code
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Confirm Detail
2
7
Lot No
2024-12-25
0
/ 600 PCS
Qty
Location : 1A-01
8
8

## Slide 25
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-7. Picking Process (Part Store)
Production Management System Pegasus
Start
Yes
Check daily job?
Outbound process scan by handy
All done?
No
Yes
Place the items to production order store
No
Finish
Print the remaining label and picking label
Paste the new label
Outbound item
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Date
From
1
2
- Display suggest FIFO
The printed label here will have the QC inspection results.
9

## Slide 26
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-8. Crusher Picking Process (Injection Store)
Production Management System Pegasus
Start
Yes
Need to use the crusher?
Crusher Outbound process scan by handy from production store
All done?
No
Yes
Feed the outbound material to the machine
No
Finish
Print the remaining label and picking label
Paste the new label
Outbound item
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Date
From
1
2

## Slide 27
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-8. Crusher Picking Process (Injection Store)
Production Management System Pegasus
Start
Yes
Need to use the crusher?
Crusher Outbound process scan by handy from production store
All done?
No
Yes
Feed the outbound material to the machine
No
Finish
Print the remaining label and picking label
Paste the new label
Outbound item
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Date
From
1
2
Virgin 100 use25
crusher 100 use 5
WH 75 INJ 25
95 5

## Slide 28
4. Operation flow
Warehouse
4-1. Work Flow Chart
4-1-9. Mix material(Injection Store)
Injection
9
Start
Outbound virgin Page 25
Start
Inbound manual crusher
Inbound Confirm virgin
Page 24
Store in the ​​Injection area
Take out raw materials for production
Need to use the crusher?
Define Virgin and Crusher Material Ratio
Page26
Enter the production process
Mix Virgin & Crusher
No
Yes
use Virgin only
Production completed
Inbound WIP Page 23
Store in
the Injection area
Move WIP to WH
Inbound Confirm WIP Page 24
Store WIP in Warehouse location.

## Slide 29
4. Operation flow
Warehouse
4-1. Work Flow Chart
4-1-9. Injection Work Process (Injection Store)
Injection
9
Start
Outbound virgin Page 25
Start
Inbound manual crusher
Inbound Confirm virgin
Page 24
Store in the ​​Injection area
Take out raw materials for production
Print label
Inbound to store Injection
Crusher
Virgin M12210528
MIX Virgin & Crusher
Format : part code CS + percent crusher + virgin

## Slide 30
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-10. NG In Process (Assembly Store)
Production Management System Pegasus
Start
Yes
Record NG In Process?
Scan the parts NG
All done?
No
Yes
Collect and move to waste area
No
Finish
Confirm will outbound the parts from PD store
1

## Slide 31
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-11. Rework process (Return FG from customer/Defected FG at the end of ASSY line)
Production Management System Pegasus
Start
Yes
Receive defected FG?
Scan the parts FG
All done?
No
Yes
Able to use the rework parts in production
No
Finish
Adjust Qty and Confirm
1
Automatic outbound the FG label and inbound rework parts
FG-PART-01
Inbound Rework
2
PCS
Qty

## Slide 32
4. Operation flow
YAMATO
4-1. Work Flow Chart
4-1-12. Rework NG process (Return FG from customer/Defected FG at the end of ASSY line)
Production Management System Pegasus
Start
Yes
Receive defected FG?
Scan the parts FG
All done?
No
Yes
Collect and move to waste area
No
Finish
Adjust Qty and Confirm
1
Inbound Rework NG
PCS
Qty
Automatic outbound the FG label and inbound NG parts

## Slide 33
4. Operation flow
YAMATO
Production Management System Pegasus
Change Location
Stock taking
Stock check
4-2. Stock management
HT : Change Location
HT : Stock taking
HT : Stock Check

## Slide 34
4. Operation flow
4-3. Outbound
Manage inbound status using the following 3 steps.
Cancel
Outbound Completed
Schedule registered
Outbound working

## Slide 35
4. Operation flow
YAMATO
Production Management System Pegasus
4-4. Master management
Location master
User master
User credential master
Authority master
Name master
Packing Standard master
PC : Location master
PC : User master
PC : User Credential
PC : Authority Master
PC : Name Master
PC : Packing Standard
BOM master
PC : Package Type
Item master
PC : Item master
Defect master
PC : Defect master
8

## Slide 36
5. System functional specifications
5-1. Handy terminal function
1. User Login
2. Main menu
3. Inbound menu
4. Outbound menu
5. Stock management menu
Work Outbound
Delivery Outbound
Outbound Manual
Inbound
6. Inbound Item
Schedule Label
Label Manual
Inbound Manual
Inbound Schedule
Inbound Item
Date
From
Date
To
Supplier
code
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
SCHEDULE
MANUAL
SCHEDULE
MANUAL
QC Check
PHOTO
7. Inbound Detail
Work Outbound
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Lot no : 20231225, 20240118
Order No : DEMO-ORDER-NO-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Lot no : 20231225, 20240118
Date
From
8. Work Outbound
9. Outbound Detail
10. Stock check
11. Stock taking
12. Change location
Inbound Schedule
Inbound Rework
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No:
6,860
DEMO-PARTS-NO_B
3
Inbound Schedule
Inbound Rework NG
Lot No
2024-12-25
0
KGS
Qty
0
KGS
NG
Total 0/600 KGS
3
8
Confirm Inbound
Label For Return
8

## Slide 37
5. System functional specifications
5-1. Handy terminal function
5-1-1. User Login
This is the screen that transitions after icon app click from home screen.
User name: Information is referenced from the User master.
Enter the User code of User master.
If it enter a code that does not exist, an error screen will be displayed. *1
Pass word: Information is referenced from the User credential master.
The User code of User master is linked to the User code of User credential master. User credential Enter the master password.
If it enter a code that does not exist, an error screen will be displayed. *1
Login button: If the information is correct, it will be redirected to the Main menu.
User master
User credential master
*1: Display screen when information is incorrect
OK button: Close this screen. Return to the previous process.

## Slide 38
5. System functional specifications
5-1. Handy terminal function
5-1-2. Main menu
admin
1234
This is the screen that transitions after logging in from User Login.
Inbound button: Transitions to the Inbound screen.
Outbound button: Transitions to the Outbound screen.
Stock Management button: Transitions to the Stock Management screen.
Close button: Closes the application.

## Slide 39
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-1. Inbound
This is the screen that transitions after select inbound from Main menu.
Inbound Schedule button: Transitions to the Inbound Schedule screen.
Inbound Manual button: Transitions to the Inbound screen.
Inbound Rework button: Transitions to the Inbound Rework screen.
< (P1): Back to Main menu
Schedule Label
Label Manual
Inbound Schedule
Inbound Manual
Inbound Schedule
Inbound Schedule
Inbound Rework
3
Inbound Schedule
Inbound Rework NG
Inbound Schedule
QC schedule
7

## Slide 40
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-2. Inbound Item
Inbound item
This is the screen that transitions after select Inbound Schedule from Inbound.
Date from: Select the start of the target date. Default is today's date. Search ORDER DELIVERY DATE
Date to: Select the end of the target date. Default is today's date. Search ORDER DELIVERY DATE
Supplier code: Select supplier code. Or do a scan. Default is blank. Search SUPPLIER CODE
Except complete: If checked, the completed status Item list will not be displayed from the Item list. Default is unchecked.
Order list : Display a list that matches the condition.
Order no : ORDER NO
Supplier name : SUPPLIER CODE
Part No.: PART NUMBER
Part Name: PART NAME
Location: Fixed location of each Item linked to Item master
Item quantity: Number of items that have been processed
Status color: Green - Completed, Dark Blue - Working, Light Blue - Not Started.
< (P1): Back to Main menu
Date
From
Date
To
Supplier
code
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Schedule Label
Label Manual
Inbound Schedule
Inbound Manual
Inbound Schedule
Inbound Schedule
Inbound Rework
3
Inbound Schedule
Inbound Rework NG
QC schedule

## Slide 41
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-3. Inbound Detail [for Inbound material to WH]
This is the screen that transitions after select order information from Inbound screen.
Part No.: Part number
Part Name :PART NAME
Lot No: Today date YYYY-MM-DD will be default
Qty: Quantity of received item
Unit: Receive unit will be loaded from schedule
Total Qty: Will be loaded from schedule
Location : The allowed location and free location will be loaded from the Location master. No initial value information.* The location control will be identified in QR Code
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
Inbound item
Date
From
Date
To
Supplier
code
status
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Lot No
2024-12-25
(Step.4) confirm
press the confirm button
600
KGS
Qty
Total 600/600 KGS
Lot No
2024-12-25
0
KGS
Qty
Total 0/600 KGS
Lot No
2024-12-25
500
KGS
Qty
Total 600/600 KGS
8
After scan label
change background color to green (GOOD/NG)
8
100
NG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
QC
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Lot No
2024-12-25
500
KGS
Qty
Total 600/600 KGS
100
KGS
NG
(Step.1) Print Label
Select schedule Enter the quantity then
press the print label button.
QC records inspection results on the web page.
8
(Step.2) QC Result
Select a Schedule that has passed QC. The system will show the QC inspection results in the inbound detail page.
8
Show results
of each type
The system will inbound into the QC location. LOCATION QC = IQC (incoming QC) *Every time you have to do QC*
9
9
Qty OK : Inbound to selected location Qty NG : Outbound from IQC location
9
(Step.3) Inbound
Scan labels and
scan storage locations
9

## Slide 42
5. System functional specifications
5-2. Handy terminal function Inbound
5-2.4-. Inbound Detail [for Assy Inbound FG to WH]
This is the screen that transitions after select order information from Inbound screen.
Part No.: Part number
Part Name :PART NAME
Lot No: Today date YYYY-MM-DD will be default
Qty: Quantity of received item
Unit: Receive unit will be loaded from schedule
Total Qty: Will be loaded from schedule
Location : The allowed location and free location will be loaded from the Location master. No initial value information.* The location control will be identified in QR Code
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
Inbound item
Date
From
Date
To
Supplier
code
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P2]
Lot No
2024-12-25
600
KGS
Qty
Total 600/600 KGS
Lot No
2024-12-25
0
KGS
Qty
Total 0/600 KGS
Lot No
2024-12-25
600
KGS
Qty
Total /600 KGS
8
QC records inspection results on the web page.
0
KGS
NG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
QC
When you press Confirm, the system will automatically outbound the material used by
the calculation according to the BOM. *If the material is at L3, it must be possible to
add an additional Outbound quantity.
OK
Show Part name.
8
KG
Outbound Purge / Set up
System : 5 KG
The system must outbound
this item by 8 KG.
Inbound Production to WH
status
8
(Step.1)
Select schedule Enter the quantity then press the confirm button
9
Default : As calculated by the system
*If no data is entered or zero is entered, the system will outbound as initially calculated.
9
(Step.2)
Select the Schedule again that has been verified.
(Step.3) Print Label
Click the print label button
For printing label.
Show results
of each type
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
600
KGS
Qty
Total 600/600 KGS
After scan label
change background color to green (GOOD/NG)
9
(Step.4) Inbound
Scan labels and scan storage locations
After that press the confirm button
0
KGS
NG

## Slide 43
5. System functional specifications
5-2. Handy terminal function Inbound
5-2.5-. Inbound Detail [for Injection or Press Inbound WIP to WH]
Inbound item
Date
From
Date
To
Supplier
code
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
580
KGS
Qty
Total 0/600 KGS
Lot No
2024-12-25
0
KGS
Qty
Total 0/600 KGS
QC records inspection results from a total of 580 products on the web page.
0
KGS
NG
20
KGS
NG
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
600
KGS
Qty
Total 600/600 KGS
0
KGS
NG
How to input defect details
Please select defect.
Defect3
10
Defect1
5
Defect2
5
Add
X
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Finishing / Tapping
Print label [P1]
200
KGS
OK
Total 0 / 580 KGS
8
80
KGS
NG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 600.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 0.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 0.00/600.00 KG
QC
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 560.00/600.00 KG
status
(Step.1) Enter Qty
Select schedule Enter the quantity then press the confirm button
Condition Outbound
Same as page 39
Please select the next process.
QC
Finishing
(Step.2) Select next process
After press the confirm button.
The system will prompt you to select the next process.
(Step.3) If selected Finishing or Tapping
Select the Schedule again
then enter the quantity
After that press the confirm button.
*At this process, the quantity can be split into multiple transactions.
(Name button or page)
Finishing : for Injection.
Tapping : for Press.
Next page
9
8
9
9
Lot No
2024-12-25
9
Yellow background for finishing or Tapping work.
QC records inspection results from a total of 280 products on the web page.
1
2
1
2

## Slide 44
5. System functional specifications
5-2. Handy terminal function Inbound
5-2.5-. Inbound Detail [for Injection or Press Inbound WIP to WH]
Inbound item
Date
From
Date
To
Supplier
code
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
100
KGS
Qty
Total 380/600 KGS
50
KGS
NG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 600.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 380.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 0.00/600.00 KG
QC
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 560.00/600.00 KG
status
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
QC Result
Print label [P1]
Lot No
2024-12-25
560
KGS
Qty
Total 560/600 KGS
0
KGS
NG
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Finishing / Tapping
Print label [P1]
KGS
OK
Total 580 / 580 KGS
KGS
NG
Lot No
2024-12-25
QC
9
Only items with QC inspection results and have not been inbound can be selected.
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
100
KGS
Qty
Total 380/600 KGS
(Step.4)
Select the Schedule again.
Then click print label button.
Then select the item want to print label
50
KGS
NG
After scan label
change background color to green (GOOD/NG)
(Step.5) Print label
click print label button.
Show results
of each type
(Step.6) Inbound
Scan labels and scan storage locations
After that press the confirm button
For work need to do in finishing / tapping process
For work not need to do in finishing / tapping process
Inbound item
Date
From
Date
To
Supplier
code
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-B
Supplier Name : DEMO-SUP-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 600.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 380.00/600.00 KG
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 0.00/600.00 KG
QC
Order No : DEMO-ORDER-NO-A
Supplier Name : DEMO-SUP-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Location : AE01 560.00/600.00 KG
status
QC
Act Qty
Qty
2023-09-28
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
200
Act Qty
Qty
Inbound Detail
Print label [P1]
Lot No
2024-12-25
580
KGS
Qty
Total /600 KGS
0
KGS
NG
(Step.) Print label
click print label button.
Show results
of each type
1
2
1

## Slide 45
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-6. Inbound Rework
This is the screen that transitions after select order information from Inbound screen.
Part No.: Part number
Qty: Quantity of total NG items for rework.
Unit: Unit of NG items qty.
Location : The allowed location and free location will be loaded from the Location master. No initial value information.* The location control will be identified in QR Code
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
Inbound Rework
Operation completed
INFORMATION
PCS
Qty
FG-PART-01
Inbound Rework
2
PCS
Qty
Inbound Rework
PCS
Qty
FG-PART-01
Inbound Rework
2
PCS
Qty
OK
Cancel
Part no 2
QTY
10
PCS
LOT NO
2023-09-09
FG-PART-01
Inbound Rework
2
PCS
Qty
* Able to enter 0 to discard some items
5

## Slide 46
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-7. Inbound Rework NG
This is the screen that transitions after select order information from Inbound screen.
Part No.: Part number
Qty: Quantity of total NG items for rework.
Unit: Unit of NG items qty.
Location : The NG locations will be loaded from the Location master. No initial value information.* The location control will be identified in QR Code
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
Inbound Rework NG
Operation completed
INFORMATION
PCS
Qty
FG-PART-01
Inbound Rework NG
2
PCS
Qty
Inbound Rework NG
PCS
Qty
FG-PART-01
Inbound Rework NG
2
PCS
Qty
OK
Cancel
Part no 2
QTY
10
PCS
LOT NO
2023-09-09
FG-PART-01
Inbound Rework NG
2
PCS
Qty
* Able to enter 0 to discard some items
3
NG Locations will be loaded.
5

## Slide 47
5. System functional specifications
5-2. Handy terminal function Inbound
5-2-8. Confirm Inbound schedule
This is the screen that transitions after select order information from Qc screen.
Part No.: Part number
Part Name :PART NAME
Lot No: Today date YYYY-MM-DD will be default
Qty: Quantity of received item
Unit: Receive unit will be loaded from schedule
Total Qty: Will be loaded from schedule
Location : The allowed location and free location will be loaded from the Location master. No initial value information.* The location control will be identified in QR Code
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
Confirm Detail
8
*Recommended location
for storing in warehouse
By Item Master
(Step.1)
Scan all of the label to confirm the detail
(Step.2)
Scan the location you want to store.
Location : A0102
Change background color to green
(Step.4)
Click the Confirm[P4] to complete the operation
Operation completed
INFORMATION
Confirm Inbound
Confirm Inbound
Confirm Inbound
Confirm Inbound
Confirm Inbound

## Slide 48
Work Outbound
Delivery Outbound
Outbound Manual
Inbound
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-1. Outbound
This is the screen that transitions after select outbound from Main menu.
Work Outbound: Transitions to the Work Outbound screen.
Production Outbound: Transitions to the Production Outbound screen.
Outbound Manual button: Transitions to the Outbound manual screen.
< (P1): Back to Main menu

## Slide 49
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-2. Work Outbound
This is the screen that transitions after select outbound schedule from Outbound menu.
Target items: For outbound items feed to the production line.
Date from: Select the start of the target date. Default is today's date. Search ORDER DELIVERY DATE
Date to: Select the end of the target date. Default is advance 7 days date. Search ORDER DELIVERY DATE
Except complete: If checked, the completed status Item list will not be displayed from the Item list. Default is unchecked.
Order list : Display a list that matches the condition.
Order no : ORDER NO
Part No.: PART NUMBER
Part Name : PART NAME
Lot No: *Displays a list of Lot no that are recommended for picking after reservation. If there are multiple items, display multiple items.
Location: *Display assigned location information. If there are multiple items, display multiple items.
Item quantity: Number of items that have been processed "/" ORDER QTY(PER UNIT)
Status color: Green - Completed, Dark Blue - Working, Light Blue - Not Started.
< (P1): Back to Main menu
Work Outbound
Date
From
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Lot No : 20230910
Location code : RD07/RD08 500.00/500.00PCS
Order No : DEMO-ORDER-NO-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Lot No : 20230910 / 20230911
Location code : RD05/RD06 0.00/600.00PCS
Work Outbound
Delivery Outbound
Outbound Manual
Inbound

## Slide 50
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-3. Delivery Outbound
This is the screen that transitions after select outbound schedule from Outbound menu.
Target items: For delivery order items
Date from: Select the start of the target date. Default is today's date. Search ORDER DELIVERY DATE
Date to: Select the end of the target date. Default is advance 7 days date. Search ORDER DELIVERY DATE
Except complete: If checked, the completed status Item list will not be displayed from the Item list. Default is unchecked.
Order list : Display a list that matches the condition.
Order no : ORDER NO
Part No.: PART NUMBER
Part Name : PART NAME
Lot No: *Displays a list of Lot no that are recommended for picking after reservation. If there are multiple items, display multiple items.
Location: *Display assigned location information. If there are multiple items, display multiple items.
Item quantity: Number of items that have been processed "/" ORDER QTY(PER UNIT)
Status color: Green - Completed, Dark Blue - Working, Light Blue - Not Started.
< (P1): Back to Main menu
Work Outbound
Delivery Outbound
Outbound Manual
Inbound
Delivery Outbound
Date
From
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Lot No : 20230910
Location code : RD07/RD08 500.00/500.00PCS
Order No : DEMO-ORDER-NO-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Lot No : 20230910 / 20230911
Location code : RD05/RD06 0.00/600.00PCS

## Slide 51
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-4. Outbound Detail for Work Outbound * Same as Delivery Outbound
Work Outbound
Date
From
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Lot No : 20230910
Location code : RD07/RD08 500.00/500.00PCS
Order No : DEMO-ORDER-NO-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Lot No : 20230910 / 20230911
Location code : RD05/RD06 0.00/600.00PCS
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
This is the screen that transitions after select order information from Outbound item.
Date : Today’s date
Part No.: PART NUMBER
Part Name : PART NAME
Location Plan :*Display assigned location information. If there are multiple items, display multiple items.
Lot Plan :*Displays a list of Lot no that are recommended for picking after reservation. If there are multiple items, display multiple items.
Lot No: No initial value information * Scan QR data or Can be changed manually
Package Qty: No initial value information * Scan QR data or Can be changed manually
Package: No initial value information * Scan QR data or Can be changed manually
Sum Qty: No initial value information * Scan QR data or Can be changed manually
Location: The initial value is referenced from the Location master. No initial value information. If there is no link, display blank.* Scan QR data or Can be changed manually
Clear[P3]: Reset to the initial data
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
Enter QTY = 20pcs
Label 1 piece
Lot 2023-09-10
*3: When Parts No does not match the Plan.
OK button: Close this screen. Return to the previous process.
Parts No does not match Plan
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Lot No
Lot No
Plan
Parts Name
DEMO-PARTS-NO_B
RD05
RD06
2023-09-10
2023-09-11
0001
2
PCS
20
2023-09-10
220(Outbound QTY)
100  SCAN (use an old label)
120
100  SCAN (use an old label)
20
100  REPACK
PRINT
LABEL 1  80pcs (Force print)
LABEL 2  20pcs (YES/NO)
0/50
20/50
DEMO_PARTS_NAME_B
0/50
Parts No does not match Plan
Operation completed
OUTBOUND QTY
QTY
20
/20 PCS
Confirm[P4]
INFORMATION
Operation completed!
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
Qty per box = 10pcs
Label 1 piece
Lot 2023-09-10
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
0/50
OUTBOUND QTY
QTY
30
/20 PCS
Cannot enter the EXCEED qty!
NG
OUTBOUND QTY
QTY
0
/20 PCS
Cannot enter the ZERO qty!
NG
NG :
1. Exceed the total plan
2. Exceed the suggest FIFO
3. Enter zero/blank

## Slide 52
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-4. Outbound Detail for Work Outbound * Same as Delivery Outbound
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
Enter QTY = 10pcs
Label 1 piece
Lot 2023-09-10
*3: When Parts No does not match the Plan.
OK button: Close this screen. Return to the previous process.
Parts No does not match Plan
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Lot No
Lot No
Plan
Parts Name
DEMO-PARTS-NO_B
RD05
RD06
2023-09-10
2023-09-11
0001
2
PCS
20
2023-09-10
220(Outbound QTY)
100  SCAN (use an old label)
120
100  SCAN (use an old label)
20
100  REPACK
PRINT
LABEL 1  80pcs (Force print)
LABEL 2  20pcs (YES/NO)
40/50
DEMO_PARTS_NAME_B
Parts No does not match Plan
Operation completed
OUTBOUND QTY
QTY
10
/10 PCS
Confirm[P4]
INFORMATION
All items completed!
50/50
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
RD05
RD06
2023-09-10
2023-09-11
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
0001
2023-09-10
2023-09-10
PCS
10
DEMO_PARTS_NAME_B
0/20
10/50
OUTBOUND QTY
QTY
10
/20 PCS
Confirm[P4]
PRINT LABEL
Print all remaining labels?
YES
NO
DEMO-PARTS-NO_B
Enter QTY = 10pcs
Label 1 piece
Lot 2023-09-10
INFORMATION
Operation completed!
PRINT LABEL
Print all remaining labels?
YES
NO
2 Types printed label
New (black color)
Remaining/Old (white color)
5
Qty (inside FIFO)
Label Qty < FIFO remaining Qty  Label Qty
Otherwise  FIFO remaining Qty

## Slide 53
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-4. Outbound Detail for Work Outbound * Same as Delivery Outbound
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
Enter QTY = 10pcs
Label 1 piece
Lot 2024-10-12
*3: When Parts No does not match the Plan.
OK button: Close this screen. Return to the previous process.
Parts No does not match Plan
Qty
Outbound Detail
Box No
Box no
Lot No
Location
Plan
Lot No
Plan
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
RD05
RD06
2023-09-10
2023-09-11
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Lot No
Lot No
Plan
Parts Name
DEMO-PARTS-NO_B
RD05
RD06
2023-09-10
2023-09-11
0001
2
PCS
20
2023-09-10
220(Outbound QTY)
100  SCAN (use an old label)
120
100  SCAN (use an old label)
20
100  REPACK
PRINT
LABEL 1  80pcs (Force print)
LABEL 2  20pcs (YES/NO)
40/50
DEMO_PARTS_NAME_B
Parts No does not match Plan
Operation completed
OUTBOUND QTY
QTY
10
/10 PCS
Confirm[P4]
INFORMATION
All items completed!
PRINT LABEL
Print all remaining labels?
YES
NO
50/50
* Scan the other items not included in the FIFO plan
* All status should be changed to OK while the outbound items have already completed
Qty (outside FIFO)
Label Qty < Total remaining Qty  Label Qty
Otherwise  Total remaining Qty
* Show total of label qty in case of manual outbound
5

## Slide 54
5. System functional specifications
5-3. Handy terminal function Outbound
5-3-5. Outbound Detail for INJECTION Work Outbound
Work Outbound
Date
From
Date
To
Except complete
07/Oct/2023
07/Oct/2023
Order No : DEMO-ORDER-NO-A
Parts No : DEMO-PARTS-NO_A
Parts Name : DEMO_PARTS_NAME_A
Lot No : 20230910
Location code : RD07/RD08 500.00/500.00PCS
Order No : DEMO-ORDER-NO-B
Parts No : DEMO-PARTS-NO_B
Parts Name : DEMO_PARTS_NAME_B
Lot No : 20230910 / 20230911
Location code : RD05/RD06 0.00/600.00PCS
This is the screen that transitions after select order information from Outbound item.
Date : Today’s date
Part No.: PART NUMBER
Part Name : PART NAME
Use Crusher : Enable/Disable to picking the crusher as percentage.
Location Plan :*Display assigned location information. If there are multiple items, display multiple items.
Lot Plan :*Displays a list of Lot no that are recommended for picking after reservation. If there are multiple items, display multiple items.
Lot No: No initial value information * Scan QR data or Can be changed manually
Package Qty: No initial value information * Scan QR data or Can be changed manually
Package: No initial value information * Scan QR data or Can be changed manually
Sum Qty: No initial value information * Scan QR data or Can be changed manually
Location: The initial value is referenced from the Location master. No initial value information. If there is no link, display blank.* Scan QR data or Can be changed manually
Clear[P3]: Reset to the initial data
Confirm[P4]: Confirmation processing. Normal end: Completion of registration *1. Warning: Warning screen display *2
< (P1): Back to Main menu
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
Enter QTY = 20pcs
Label 1 piece
Lot 2023-09-10
*3: When Parts No does not match the Plan.
OK button: Close this screen. Return to the previous process.
Parts No does not match Plan
Qty
Outbound Detail
Box No
Box no
Lot No
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Lot No
Lot No
Plan
Parts Name
DEMO-PARTS-NO_B
RD05
RD06
2023-09-10
2023-09-11
0001
2
PCS
20
2023-09-10
220(Outbound QTY)
100  SCAN (use an old label)
120
100  SCAN (use an old label)
20
100  REPACK
PRINT
LABEL 1  80pcs (Force print)
LABEL 2  20pcs (YES/NO)
20/50
DEMO_PARTS_NAME_B
Parts No does not match Plan
Operation completed
Confirm[P4]
INFORMATION
Operation completed!
2
Total 0/50
OUTBOUND QTY
QTY
20%
20
/20 KGS
Use Crusher
Crusher-parts-no-xx
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Box no
Lot No
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
Use Crusher
Crusher-parts-no-xx
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Box no
Lot No
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
20%
Use Crusher
Crusher-parts-no-xx
Total 0/45
Outbound Detail
Crusher P/No
Crusher-part-no-xxx
Total 0/45
Total 0/5
The FIFO and outbound details will recalculate while user uses the crusher.
Swipe up the screen to process the crusher outbound list items.
DEMO-PARTS-NO_B
Qty
Outbound Detail
Box No
Box no
Lot No
Parts No
Parts Name
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
20%
Use Crusher
Crusher-parts-no-xx
Outbound Detail
Crusher P/No
Crusher-part-no-xxx
Total 45/45
Confirm[P4]
Total 45/45
Total 5/5
It need to be process an outbound.
The Handy will allow to confirm only when the crusher item has been picked.
20%
Total 0/45
Show confirmation dialog about Reset all data if user change the ratio percentage or disable/enable.
It can be 5/10/15/20/25 which set in config file.
Referred to page 64.
CRUSHER changed detect
Click “YES” to clear all data?
YES
NO
5

## Slide 55
5. System functional specifications
5-4. Handy terminal function Stock Management
5-4-1. Stock management
This is the screen that transitions after select Stock management from Main menu.
Stock Check button: Transitions to the Stock Check screen.
Stocktaking button: Transitions to the Stocktaking screen.
Change Location button: Transitions to the Change Location screen.
< (P1): Back to Main menu
Label For Return
8
Label For Return
8

## Slide 56
5. System functional specifications
5-4. Handy terminal function Stock Management
5-4-2. Stock Check
This is the screen that transitions after select Stock check from Stock management menu.
Parts No: No initial value information, List selection from Item master* Can be changed manually or scan label
Lot No: No initial value information.* Can be changed manually or scan label
Location : No initial value information
Qty Box : No initial value information
Qty : No initial value information
Total : No initial value information
Clear[P3]: Clear input contents
OK[P4]: Confirmation processing. Search data.
< (P1): Back to Main menu
Qty
Lot No
*2: Display screen when information is incorrect
OK button: Close this screen. Return to the previous process.
Qty
DEMO-PARTS-NO_B
Qty per box = 10pcs
Label 1 piece
Lot 2023-09-09
6,850
6,860
DEMO-PARTS-NO_B
DEMO-PARTS-NO_B
3
Label For Return
8

## Slide 57
5. System functional specifications
5-4. Handy terminal function Stock Management
5-4-3. Stocktaking
This is the screen that transitions after select Stocktaking from Stock management menu.
Parts No: No initial value information, List selection from Item master* Can be changed manually or scan label
Lot No: No initial value information.* Can be changed manually or scan label
Location : No initial value information .* Can be changed manually or scan label
Qty : System quantity, No initial value information *The quantity in the system will be displayed.
Act ถty : Actual quantity, No initial value information
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing.
< (P1): Back to Main menu
808-0210031-00
Label 1 piece
Lot 2024-02-03
Instructions
Scan location
Scan label
Current stock information will be shown on screen.
Click “Confirm” to apply the information.
In the case of NG, the item was rescanned.
Success dialog will show if the data saving completed.
5
Label For Return
8

## Slide 58
5. System functional specifications
5-4. Handy terminal function Stock Management
5-4-4. Change Location
This is the screen that transitions after select Change Location from Stock management menu.
Parts No: No initial value information, List selection from Item master* Can be changed manually or scan label
Lot No: No initial value information.* Can be changed manually or scan label
Qty : No initial value information Can be changed manually or scan label
Old Location : No initial value information .* Can be changed scan label
New Location : No initial value information .* Can be changed manually or scan label
Clear[P3]: Clear input contents
Confirm[P4]: Confirmation processing.
< (P1): Back to Main menu
DEMO-PARTS-NO_B
Label 1 piece
Lot 2023-09-09
DEMO-PARTS-NO_B
Label 1 piece
Lot 2023-09-09
* Scan the same label
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
2023-09-09
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
2023-09-09
DEMO-PARTS-NO_B
Label 1 piece
Lot 2023-09-09
Serial 0001
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
2023-09-09
DEMO-PARTS-NO_B
Label 1 piece
Lot 2023-09-09
Location: LO01
Serial 0002(new serial)
120
DEMO-PARTS-NO_B
DEMO_PARTS_NAME_B
2023-09-09
200
200
200
200
200
DEMO-PARTS-NO_B
Label 1 piece
Lot 2023-09-09
Location: LO01-A
Serial 0003(new serial)
All pack change location
1
2
Partial change location
Label For Return
8

## Slide 59
5. System functional specifications
5-4. Handy terminal function Stock Management
5-4-5. Label For Return
This is the screen that transitions after select Label For Return
from Stock management menu.
Parts No: No initial value information, List selection from Item master* Can be changed manually or scan label
Lot No: No initial value information. Location : No initial value information
Qty Box : No initial value information
Qty : No initial value information
Total : No initial value information
Clear[P3]: Clear input contents
OK[P4]: Confirmation processing. Search data.
< (P1): Back to Main menu
Qty
Lot No
*2: Display screen when information is incorrect
OK button: Close this screen. Return to the previous process.
Label For Return
8
Label For Return
Print label [P2]
*Show only items in
your own department.
6,850
30-002863-00-00
Name :
Name :
Name :
Name :
CONTACT TREATMENT OIL...
6,850
Location
A001
Can edit lot number
Scan or select

## Slide 60
5. System functional specifications
5-5. PC operation flow basic
5-5-1. Login-Menu
Prepare user ID and password for YAMATO.
Please log in with YAMATO user ID and password.
Username: admin
Pass: 1234

## Slide 61
5. System functional specifications
5-5. PC operation flow basic
5-5-2. Main-Menu
[Schedule]
[Inbound]
[Outbound]
[Stock Management]
[Master Management]
Inbound Schedule Material
Stock Maintenance Inquiry / Report
Schedule
Stock management
Master management
2
3
1
4
5
Stocktaking
Stock Inquiry / report
Stock Maintenance
Supplier master
User credential master
Customer master
Location master
User master
Supplier master
Packing Standard master
Inbound Inquiry Report
Outbound Inquiry Report
Inbound
Outbound
Item master
Customer master
Department master
Purchase Instructions
Bill Of Material
Crusher Ratio master
3
3
Stock Inventory
Report
5
8
Stock Monthly Report
Weekly Delivery Report
Stock Card Report
Delivery Monthly Report
8
8
8
Calendar Master
8
8
8
Department master
8
Inbound Schedule Material
Inbound Schedule Production
Outbound Schedule Material
Outbound Schedule Delivery
8

## Slide 62
5. System functional specifications
5-6. PC operation flow Schedule
5-6-1. Inbound Schedule Material
Cancel button It can change the status to Cancel.
CSV import button It can import CSV files manually.
Add button It can register as many schedules as it manually select.
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
Status management
Cancel
Inbound Completed
Schedule registered
Inbound working
Show the clicked link if there are already process.
It will open the history preview web page.

## Slide 63
5. System functional specifications
5-6. PC operation flow Schedule
5-6-2. Inbound Schedule Production
Cancel button It can change the status to Cancel.
CSV import button It can import CSV files manually.
Add button It can register as many schedules as it manually select.
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
Status management
Cancel
Inbound Completed
Schedule registered
Inbound working
Show the clicked link if there are already process.
It will open the history preview web page.

## Slide 64
5. System functional specifications
5-6. PC operation flow Schedule
5-6-3. Outbound Schedule Material
Cancel button It can change the status to Cancel.
CSV import button It can import CSV files manually.
Add button It can register as many schedules as it manually select.
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
Status management
Cancel
Outbound Completed
Schedule registered
Outbound working
Show the clicked link if there are already process.
It will open the history preview web page.

## Slide 65
5. System functional specifications
5-6. PC operation flow Schedule
5-6-3. Outbound Schedule Delivery
Cancel button It can change the status to Cancel.
CSV import button It can import CSV files manually.
Add button It can register as many schedules as it manually select.
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
Status management
Cancel
Outbound Completed
Schedule registered
Outbound working
Show the clicked link if there are already process.
It will open the history preview web page.

## Slide 66
5. System functional specifications
5-7. PC operation flow Inbound
5-7-1. Inbound
** Standard specifics
CSV Export button Export all recodes for CSV file
PDF Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 67
5. System functional specifications
5-8. PC operation flow Outbound
5-8-1. Outbound
** Standard specifics
CSV Export button Export all recodes for CSV file
PDF Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 68
5. System functional specifications
5-9. PC operation flow Stock management
5-9-1. Stock Inquiry Report
** Standard specifics
CSV Export button Export all recodes for CSV file
PDF Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
8

## Slide 69
5. System functional specifications
5-9. PC operation flow Stock management
5-9-2. Stock Maintenance
** Standard specifics
Register Register input data.
Remove Zero Qty Remove all zero qty records.
Add Add the blank record for input the new data.
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 70
5. System functional specifications
5-9. PC operation flow Stock management
5-9-3. Stocktaking
** Standard specifics
Save button Register input data
Confirm button Confirm the current input data
Delete button Delete selected records
Recheck button Change the status to RECHECK
Start button Initial data for current month (start the new data record)
CSV Output button Export the CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 71
5. System functional specifications
5-9. PC operation flow Stock management
5-9-5. Stock Maintenance Inquiry / Report
** Standard specifics
CSV Export button Export all recodes for CSV file
PDF Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 72
5. System functional specifications
5-9. PC operation flow Stock management
5-9-6. Purchase Instructions
CSV Export button Export all recodes for CSV file
PDF Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
The system will keep the data everyday.
Shipment plan (-)
Remain PO (actual data) (inbound mat) (+)
Item master e.g. RM-Leadtime
Stockcard data (+)
4
Import PO plan
Will increase the delivery date with lead time
Able to scroll
5
Show information for every day in the next 3 months.
Link this page to notification dialog at home page
Must be enter after PO issued
Status :
1. Start
2. Temporary PO
3. PO issued - Inbound date not yet
4. PO issued - Inbound date answered
Background color :
RED : Start
YELLOW : Temporary PO / PO issued
GREEN : PO issued – date answered
3
4
2
7
100
/Total 200 pcs
Sum all need qty in selected date range
Show information for every day in the next 4 months.
8

## Slide 73
5. System functional specifications
5-9. PC operation flow Master management
5-9-7. Stock Inventory Report
CSV Export button Export all recodes for CSV file
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
Category: Item category (Item master)
Item name: Item name (Item master)
Item number: Item code (Item master)
Drawing number: Drawing number (Item master)
FG : Average shipping qty per month: Last 1 year
100 100 ;;;;;;;100 = 100
RM : (N-2) – (N-1) – Inbound Qty
100 - (120 -40) = 20 last 1year
Safety stock qty: Safety stock quantity (Item master)
Latest shipping date: Last shipping date (Outbound transactions)
Inventory quantity: Stock quantity
Unit price: Unit price (Item master)
** Standard specifics
5
Stock Inventory Report
Show popup menu
- Stock inquiry report
8

## Slide 74
5. System functional specifications
5-9. PC operation flow Master management
5-9-8. Stock monthly report (monthly inventory report)
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 75
5. System functional specifications
5-9. PC operation flow Master management
5-9-9. Weekly delivery report(Plan/Actual/Balance stock)
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 76
5. System functional specifications
5-9. PC operation flow Master management
5-9-10. Stock card (Part No., Rec, Issue, Stock)
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 77
5. System functional specifications
5-9. PC operation flow Master management
5-9-11. Delivery monthly report (PO No., FG, Name, Qty, Req-date, Delivery date
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 78
5. System functional specifications
5-10. PC operation flow Master management
5-10-1. Item master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
5
Add the below columns
Drawing no
Category

## Slide 79
5. System functional specifications
5-10. PC operation flow Master management
5-10-2. Packing Standard master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics

## Slide 80
5. System functional specifications
5-10. PC operation flow Master management
5-10-3. Supplier Master
** Standard specifics
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
8

## Slide 81
5. System functional specifications
5-10. PC operation flow Master management
5-10-4. Location master
** Standard specifics
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 82
5. System functional specifications
5-10. PC operation flow Master management
5-10-5. User master
** Standard specifics
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 83
5. System functional specifications
5-10. PC operation flow Master management
5-10-6. User Credential master
** Standard specifics
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.

## Slide 84
5. System functional specifications
5-10. PC operation flow Master management
5-10-7. Customer Master
** Standard specifics
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
8

## Slide 85
5. System functional specifications
5-10. PC operation flow Master management
5-10-8. Crusher Ratio master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
2
Crusher details
1. Virgin (Part No.)
2. Crusher (Part No.)
3. Ratio(%) – The default ratio of each item. It can be 5/10/15/20/25 shown in drop down list in handy.
4. Max Rate(%) – The maximum rate of crusher that able to choose in handy.
5. FG (Part No.)
* User must define the crusher information for INJECTION process
6
6
These values can be further modified which defined in the HT settings config named 'crusher_ratio’.
For example
crusher_ratio=5,10,15,20,25

## Slide 86
5. System functional specifications
5-10. PC operation flow Master management
5-10-9. BOM master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
5

## Slide 87
5. System functional specifications
5-10. PC operation flow Master management
5-10-10. Calendar master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 88
5. System functional specifications
5-10. PC operation flow Master management
5-10-11. Department master
CSV Import button Import selected CSV file
CSV Export button Export all recodes for CSV file
Delete button Delete selected records
Edit mode button Transitions to edit screen mode
Save button Save data
Search button Search using the entered conditions.
Clear button Initializes and clears the entered conditions.
** Standard specifics
8

## Slide 89
6. Q&A

## Slide 90
7. Sign off
We hereby acknowledge and agree the above-mentioned blueprint requirements.
Any changes required after the sign off for this blueprint will be addressed through the change request process.
Yamato Electric (Thailand) Co., Ltd.
Sign:
## END OF BLUEPRINT##
Name:
Title:
Date:
TOMAS TECH CO.,LTD.
Sign:
Name:
Title:
Date: