## Slide 1
┃Line notification function
1.1 Notify Line Notify when the patrol light is red.
1.2 Notify Group A if red, Group B if blue. Separate accounts.
2.1 Sending jpeg data at the same time as the error message
2.2 Sending jpeg data with the "Camera No" and "pic" commands
2.3 Capture camera data and send jpeg data from CA01 with ``Camera No'' and ``pic'' commands
3 Distinguish the person in charge from the sender.
4 Send videos. Same as item 2.

## Slide 2
┃Line notification function
Notify the machine equipment side to Line.
１
2
3
4
6
Equipment error occurred
Line: MC20
Machine number: OP10
Error information:
Motor overheat
C
B
A
Calling the group in charge Example: Group B
NO
NO
YES
NO
The person who received the Line replies that it can respond.
Workers who answered YES head to the site. Corresponding start.
Press the completion button on Smart Watch. Complete the response.
5
Fix completed
Fix start
By collecting the rush time, response start time, and response completion time, each work time can be recorded as a log.
Response time
Start time
Finish time
Arrival time
Fix time
02-Aug-2022 14:00:00
02-Aug-2022 14:05:00
02-Aug-2022 15:05:00
00:05:00
01:00:00
An error has occurred in the equipment. Transfer information to the server for line, machine number and error information.

## Slide 3
┃Line notification function
Notify the machine equipment side to Line.
１
2
Equipment error occurred
Line: MC20
Machine number: OP10
Error information:
Motor overheat
Photo data request
MC001
PIC
An error has occurred in the equipment. Transfer information to the server for line, machine number and error information.

## Slide 4
┃Line maintenance note
Create line maintenance notes.
Detect errors from equipment. Notify the line.
Send and receive automatic messages according to the master settings on the line.
1. Equipment error notification
2. Assignment of personnel
Have you arrived?
Have you arrived?
Yes
3. Question 【1】
3. Answer 【1】

## Slide 5
┃Line maintenance note
What kind of problem?
Please tell me the reason.
Need a repair?
Yes
The cutting tool of the equipment is broken.
This is due to the life of the cutting tool.
What kind of problem?
Please tell me the reason.
What kind of problem?
Please tell me the reason.
Equipment failure
Cutting tools problem
Human error
Other
3. Question 【2】
3. Answer 【2】
3. Question 【3】
3. Answer 【3】
Have you arrived?
BOT type
Is it possible to have a conversational type like BOT?
Also, can the wording be changed by the master?
Is it possible to save conversation data in DB?
Choose type
Is it possible to have a conversational type like choose?
Also, can the wording be changed by the master?
Is it possible to save conversation data in DB?
Yes
No
What kind of problem?
Please tell me the reason.
Need a repair?
The cutting tool of the equipment is broken.
This is due to the life of the cutting tool.
Yes